## Slide 2: Motivation
Broadband wireless systems provide
  High data throughput
  Increased frequency diversity for assured communications
  Spread spectrum enables LPI/LPD
However, tradition approach requires continuous spectrum to transmit and receive a broadband spectrum
  Spectrum resource is scarce
  Large truck of continuous spectrum is even less available
  Spectrum are fragmented
Split transmission spectrum from the processing spectrum

## Slide 3: Proposed Transceiver Scheme

## Slide 4: Transmitter Power Amplifier
PMEPR & PAPR
Peak power to average power ratio is time-domain phenomenon
  Change sampling frequency would linear scale the bandwidth of individual segments as well as the space between segments without changing the PMEPR
  Thus, we could just investigate the PMEPR for a given total bandwidth with the following cases
    Equal segment bandwidth
      Fix the number of segments, varying the space between segments
        Equal spacing
        Unequal spacing
      Fix the space between segments, varying the number of segments
        Equal spacing
        Unequal spacing
    Unequal segment bandwidth

## Slide 5
f1
S1
f2
S2
f3
S3
S(t ) = S1(t )+S2(t )+S3(t )
S1:
S2:
S3:
Power Envelope
of Individual Segment
is the upper bound of
S:
Power Envelope
of Segments Sum
PA
f1
S1
f2
S2
f4
S3
S3(t ) is moved to a new spectrum position:
The power envelop of each individual signal segment doesn’t change even if the spectrum position of the segment is changed.
The power envelope upper bound for a multi-segment sum signal doesn’t change, even if the spectrum positions of individual segments are moved around.
It is sufficient to investigate the peak-to-mean envelope power ratio (PMEPR) for signals of evenly divided and evenly spaced segments.
The spectrum of unevenly divided segments and/or unevenly spaced segments can be constructed from an evenly divided and evenly spaced multi-segments spectrum by moving the spectrum positions of individual or a group of segments. For example, S1 is twice the bandwidth of S2, and S3 is three times the bandwidth of S2.
Conclusion: